Technical Report

Evaluation of SDR Boards and Toolchains
 – Evaluation of the Technical Specifications –

Authors:	Sheila Christiansen
	Alexandru Csete

Date:	YYYY-MM-DD
Version:	1.0
Status:	Draft

List of Abbreviations and Symbols
DR	Dynamic range

MDS	Minimum detectable signal
NF	Noise figure

SDR	Software defined radio

# Introduction
## Purpose and Scope
During recent years, we have seen tremendous development in the availability of low cost, consumer-grade SDR hardware. Unfortunately, the low cost and the fast pace at which SDR hardware is developed does not leave much room for delivering complete turnkey solutions to the users. Hardware is often delivered as “evaluation boards” and software support is often left to third parties.
The purpose of this activity is to evaluate a selection of currently available SDR hardware and software from a satellite communications point of view, in order to provide prospective users with independent data that is often not available from the manufacturers. The evaluation includes both analytical assessments of the hardware and software capabilities, as well as lab tests supplemented by over the air usage of the systems.
The work was executed in three parts:
1. Evaluation of the technical specifications of SDR hardware
2. Over the air evaluation
3. SDR software evaluation

This report covers part 1, Evaluation of the technical specifications of selceted SDR devices.

## Selected SDR devices
The SDR devices under test were selected according to the following criteria:
- Relevant for satellite communications, most notably for CubeSat projects
- Affordable and easily available
- Variety in architecture and expected performance
The list of devices that were tested is shown in Table 1.1 below.

Device	Type	Frequency range	Bandwidth	Bits
RTL-SDR V3	RX	0.1 – 1700 MHz	3.2 MHz	8
Airspy Mini	RX	24 – 1700 MHz	6 MHz	12
SDRplay RSPduo	RX	1 kHz – 2 GHz	10 MHz	12
LimeSDR Mini	RX/TX	10 MHz – 3.5 GHz	30 MHz	12
BladeRF 2.0 Micro	RX/TX	70 MHz – 6 GHz	56 MHz	12
Ettus USRP B210	RX/TX	70 MHz – 6 GHz	56 MHz	12
PlutoSDR	RX/TX	70 MHz – 6 GHz	56 MHz	12

Table 1.1: SelectedSDR devices under test.

## Evaluation Criteria
Given the scope of the activity, the evaluation of the devices was limited to the frequency bands used for satellite communications:
- VHF: 145-146 MHz
- UHF: 435-438 MHz
- L-band: 1.26-1.30 GHz
- S-band: 2.0-2.1 GHz TX and 2.2-2.3 GHz RX
- S-band: 2.40-2.45 GHz
- C-band: 5.8 GHz

The evaluation criteria according to which the devices are evaluated are grouped in three groups:
Generic parameters (extracted from datasheets):
  - Frequency range, stability, and phase noise
  - Maximum bandwidth
  - Operating temperature range
  - Const and availability
  - Size and weight
Receiver-specific parameters (tested):
  - Noise figure (NF) and minimum detectable signal (MDS)
  - Receiver dynamic range
  - Spectral purity
Transmitter-specific parameters (tested):
  - Maximum output power
  - Spectral purity
  - Achievable MER
## Evaluation Methods
One of our objectives with this activity was to provide useful and reproducible results. To that end, we have defined our test procedures according to the following criteria:
1. Use simple methods that do not require a lot of expensive laboratory equipment.
2. Carry out the tests under realistic conditions that are representative for a setup under which the SDR devices are normally used.
Such methods can not provide results with the same accuracy as measurements carried out in a professional RF laboratory. However, in order to increase confidence in our results, we cross-check the measurements using different test methods and tools. These cross-checks are described in section 4.
Furthermore, since we use the same methods to test all devices, the results can always be used for a relative comparison between the devices, even if the absolute
# Test Setup and Procedures
## Receiver Noise Figure
## Receiver Dynamic Range
Note: Receiver gain compression could not be measured because ADC full scale was reached before any gain compression could be observed.
## Receiver Spectral Purity
## Transmitter Spectral Purity
## Transmitter Outout Power
## Transmitter MER
## Test Software
# Test Results
## RTL-SDR V3
Alex: General description of the device and its architecture
Sheila: Technical specifications
### Receiver Noise Figure
### Receiver Blocking Dynamic Range
### Receiver Spectral Purity
### Transmitter Spectral Purity
### Transmitter Output Power
### Transmitter MER

## Airspy Mini
## SDRplay RSPduo
## LimeSDR Mini
## BladeRF 2.0 Micro
## Ettus USRP B210
## PlutoSDR
# Test Setup Verification
- We used two different methods to measure the noise figure (MDS and Y-factor)
- We used two different signal generators
- Cross check noise figure measurements at 2.4 and 5.6 GHz in wifi free zone
- Cross check measurements with the test software using another SDR software (SDR Radio V3)
# Conclusion

# Appendices
Appendix I: Heading of this appendix

# Bibliography
Primary sources

Secondary sources

Last name, first name (year): Title, Place, URL: http://www.templates.services.openoffice.org [Accessed 19/12/2019].

Curriculum vitae